## Slide 1
KX-NS PBX Remote IP Extension
June 2, 2014
Specifications are subject to change without notice.
Panasonic System Networks PBX SE team
Notes: 1

## Slide 2
Remote Office or Mobile Internet
192.168.0.1
Local Office
1. Overview
LAN
LAN
WAN 22.33.44.55
192.168.0.101
Built-in MRG feature supports remote IP extension without VPN. MRG = Media Relay Gateway Following phones support this feature. - KX-NT543/NT546/NT560 (Version up of phone software is required.) - KX-NT511 and KX-NT550 series - KX-UT series - 3rd party SIP phone with Blank UDP transmit capability. (Video phone is also supported.) Other phones do not support this feature. KX-UDT / KX-NT300 series / KX-NT300 based software phone
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
KX-NS1000 : Version 3 or later Other KX-NS PBX : Any Version
IP address in this document is example.
Notes: 2

## Slide 3
192.168.0.1
Local Office
2. Concept of Programming
LAN
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
Only 3 PBX programming are required for remote connection. (1) PBX has to know global IP address of router. 11.22.33.44 (2) Do not forget setting of default gateway. 192.168.0.1 (3) PBX has to know location of each IP extension. Local or Remote Port Fwd is required to router. (Not only 15060)
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
“5060” is too famous as port for SIP. “5060” has high risk for attacking by hacker. KX-UT in remote location uses port “15060” to access PBX through router. This document uses “15060” for other SIP phone also.
15060 to 192.168.0.101:5060
Ext 103
Remote Office or Mobile Internet
Notes: 3

## Slide 4
Chapter 1 PBX Programming

## Slide 5
11. Assign Global IP Address of Router.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Default is OK.
Notes: 5

## Slide 6
12. Assign Default Gateway.
Default gateway is required not only for remote IP extension but also for many other purpose.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Notes: 6

## Slide 7
13. Assign Location of SIP Extension.
< 3rd party SIP Phone >
192.168.0.1
Local Office
Remote Office or Mobile Internet
LAN
LAN
WAN 22.33.44.55
192.168.0.101
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Notes: 7

## Slide 8
14. Assign Location of KX-NT500.
< KX-NT500 >
Notes: 8

## Slide 9
15. Assign Location of KX-UT.
SBC : Session Boarder Controller (3rd party equipment is required.) Secure communication is available using HTTPs for KX-UT. - TR069(CWMP) is available with https. - Maximum 20 KX-UT phone can use this feature. Each one KX-NS1000 in one-look network supports 20 KX-UT with this feature.
< KX-UT >
Notes: 9

## Slide 10
Chapter 2 SIP Phone Setting
SIP Software Phone for Smart-phone by Media5 is used in this chapter as example.

## Slide 11
21. Configure SIP Account.
Notes: 11

## Slide 12
Title = Reference Username = Extension Number Password = SIP Password of PBX
See next page.
22. Assign Ext Number & PIN to log-in.
Notes: 12

## Slide 13
23. Assign Destination to log-in.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Notes: 13

## Slide 14
24. Enable “rport”.
Notes: 14

## Slide 15
Chapter 3 KX-NT/UT Phone Setting

## Slide 16
31. KX-NT500 : Assign Router as Destination.
Assign global IP address of router (11.22.33.44 for example) as destination instead of PBX local address (192.168.0.101 for example), when KX-NT phone is installed in remote office.
192.168.0.1
Local Office
Remote Office or Mobile Internet
LAN
LAN
WAN 22.33.44.55
192.168.0.101
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Notes: 16

## Slide 17
192.168.0.1
Local Office
Remote Office
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
1. Connect KX-UT phone in local office. (Not remote office) 2. Change PBX setting for this extension from “Local” to “Remote”. 3. Restart KX-UT by power off and on again. Error may display but OK. 4. Dispatch KX-UT to remote office. Destination from remote office (11.22.33.44:15060 for example) is automatically informed to KX-UT phone from PBX at step 3.
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Ext 102 192.168.1.201
32. KX-UT : Connect in Local Office.
11.22.33.44 Port : 15060
Operation is not required in remote office to connect KX-UT phone to PBX. All you have to do is to connect KX-UT phone to LAN in remote office.
Step 4 Dispatch
Notes: 17

## Slide 18
Chapter 4 Router Programming
Port forwarding is required for router.

## Slide 19
Protocol | Range of port number (WAN) | Destination | Description
RTP | 16000-16511(UDP) | 192.168.0.102 | to DSP#1-1
 | 16512-17023(UDP) | 192.168.0.103 | to DSP#1-2
 | 17024-17535(UDP) | 192.168.0.104 | to DSP#2-1
 | 17536-18047(UDP) | 192.168.0.105 | to DSP#2-2
41. Port Fwd to DSP
< for 3rd party SIP Phone / KX-NT500 / KX-UT >
< Reference of PBX setting > Default is OK. This parameter is common for IP trunk and IP extension.
WAN
LAN

## Slide 20
Port number conversion is required from 15060 to 5060.
42. Port Fwd to PBX LAN : SIP
Protocol | Port number | Destination
SIP | 15060(UDP) | 192.168.0.101:5060(UDP)
< for 3rd party SIP Phone >
< Reference of PBX setting > Default is OK.

## Slide 21
Protocol | Port number | Destination
MGCP | 2727(UDP) | 192.168.0.101
PTAP | 9300(UDP) | 192.168.0.101
43. Port Fwd to PBX LAN : KX-NT500
< for KX-NT500 >
< Reference of PBX setting > Default is OK.

## Slide 22
Protocol | Port number | Destination
SIP | 15060(UDP) | 192.168.0.101:5060(UDP)
CWMP (HTTP) | 7547(TCP) | 192.168.0.101
CWMP (HTTPS) | 37547(TCP) | 192.168.0.101
SIP-MLT Data Download (HTTP) | 7580(TCP) | 192.168.0.101
SIP-MLT Data Download (HTTPS) | 37580(TCP) | 192.168.0.101
NTP | 123(UDP) | 192.168.0.101
44. Port Fwd to PBX LAN : KX-UT
< for KX-UT >
< Reference of PBX setting > Default is OK.

## Slide 23
45. Port Fwd to PBX LAN : KX-UT
< Reference of PBX setting > Default is OK. (These should be blank.)
This is applied to above, if above is blank.

## Slide 24
46. Condition for External Router
Condition for external router is only as follows.
- Many port fwd setting is required as previous pages.
But some router does not have enough number of port fwd setting.
(Range setting is not possible.)
- New router has "SIP ALG" feature.
But this feature should be disabled by programming. - Some router by Cisco (Not all router by Cisco) does not have compatibility for KX-NT500 remote connection. When MRG feature does not work for KX-NT500, please contact us.

## Slide 25
Chapter 5 KX-NS1000 Built-in Router
MRG feature can work with KX-NS1000 built-in router.

## Slide 26
Local Office
51. Concept of Programming
LAN
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
Programming (1) and (3) are required for remote connection. (1) PBX has to know global IP address of router. 11.22.33.44 (2) Default gateway programming 192.168.0.101 (No need) (3) PBX has to know location of each IP extension. Local or Remote Fixed global IP address for WAN is required as next page. 11.22.33.44 Other settings such as Port Fwd are NOT required.
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Remote Office or Mobile Internet
Activation key KX-NSN101 is required to use WAN.
Notes: 26

## Slide 27
52. IP Address for WAN
Notes: 27

## Slide 28
Thank you !

## Slide 29
Revision
Date | No. | Change
April 17 | All | First release
May 5 | 46 (Page 24) | Condition for Cisco router was added.
June 2 | 46 (Page 24) | Condition for Cisco router was revised.
Notes: 29